## Slide 1
Lecture 7
Physics-based modelling of cell electrochemistry and ageing
Lecture 8
Battery thermal modelling
Yicun Huang, researcher
Department of Electrical Engineering
Chalmers University of Technology, Sweden
TRA 445
Advanced Battery Modelling and Control

## Slide 2: Outline
Overview of physics-based modelling
Working principles of electrochemical cells
Survey of commercial/open-source tools
Challenges of physics-based models
Single particle model (SPM)
  Solid-state diffusion
  Ion exchange kinetics
  Ageing
Reduced order modelling
  Numerical methods
  Single bucket model

## Slide 3
Two approaches to discovering physical models
Data-driven
  Kepler's law of planetary motion
  Coulomb's law
  Ohm's law
  Ideal gas law
  Butler-Volmer
First-principle
  Fourier Diffusion
  Principle of least action
  Coupled ion-electron transfer (CIET) theory
3
Lecture 5 v.s. lecture 7
Data-driven v.s. first-principle
Notes: Transformer (for example, “ChatGPT”) They power a new generation of data-driven analytics. Not just a gimmick but a workhorse. However, this approach of discovering underlying input-output relations is not new:
Kepler dedicated 20 years of observation and discovered his laws of planetary motion. E.g. the square of orbital period is directly proportional to the cube of the longest radius R.

## Slide 4
Physics-based modelling: broad area of research
Notes: Categorise them from
Battery modeling is a broad area of research. We categorise them from atomic scale all the way to system scale modelling.

## Slide 5
Physics-based modelling: broad area of research
Materials Science
SEI growth
Li plating
Mechanical aging
Automatic Control
Cell modelling
Cell control
SoX estimation
Capacity fade
Resistance rise
EIS
Cell balancing
Thermal gradient
Cooling system
Pack modelling
Industrial focus
Efficiency
Safety
User habits
V2X
Interaction with environment
Electrical potential
Diffusion
Charge transfer
Notes: In materials science, we care about …
At automatic control, we are dealing with …
In industry, …
They all play a crucial role in optimizing battery performance, improving safety, and extending the lifespan of batteries across applications like electric vehicles and energy storage systems.

## Slide 6: Where does physics-based cell modelling fit into BMS?
ECM
STAY HERE!
voltage
current
temperature
Tmin
Tmax
imin
imax
vmax
vmin
current
voltage
ECM + thermal
STAY HERE!
STAY HERE!
Physics-based
voltage
current density
anode potential
surface concentration
core temperature
Stage I graphite

## Slide 7: Where does physics-based cell modelling fit into BMS?
Notes: Battery Models Integration:
Physics-based models, such as detailed electrochemical and thermal models, capture internal battery dynamics for accurate predictions.
Reduced-order models simplify these complex models to achieve real-time performance.
State Estimation (SOC, SOH, SOT):
Physics-based models help estimate crucial battery states:
  State of Charge (SOC): Energy remaining in the battery.
  State of Health (SOH): Battery capacity degradation.
  State of Temperature (SOT): Temperature prediction to maintain safe operating conditions.
Thermal Model for Safety and Efficiency:
Physics-based thermal models enable precise heat management for avoiding overheating and thermal runaway.
Supports the thermal management system to maintain optimal temperature ranges.
Cell Balancing:
Accurate modeling helps design balancing algorithms by predicting individual cell behaviors and thermal gradients.
Sensor Interface and Real-Time Monitoring:
Measured parameters (voltage, current, and temperature) are compared with model predictions to correct errors and provide robust state estimation.
Control and Communication:
Model-based insights are communicated via the CAN bus for BMS functions, ensuring safer battery operations.

## Slide 8
Battery models: Multiphysics
Harris et al. (2010). Chem. Phys Letter.
Electrical
Electrochemical
Aging
Mechanical & Thermal
Multiphysics are commonly dynamically coupled inside a battery cell, maybe in different timescales.
[Zou, C., Manzie, C., & Nešić, D. IEEE Transactions on Control Systems Technology, 2016]
Lecture 7
Lecture 8
Notes: Battery systems are multiphysics in nature.
Electrical Behavior: This involves the current-voltage relationship, impedance characterization. Well-understood and fundamental to the delivery of power and energy storage.
Electrochemical: Chemical reactions and ion transport within the battery. （Chromogenic --》 phase change)
Aging: Long-term degradation and lifespan considerations.

## Slide 9: Outline
Overview of physics-based modelling
Working principles of electrochemical cells
Challenges of physics-based models
Single particle model (SPM)
  Solid-state diffusion
  Ion exchange kinetics
Reduced order modelling
  Numerical methods
  Single bucket model

## Slide 10: Working principles of electrochemical cells: materials
cylindrical
Notes: Terminalology:
Electrical engineering: Neg sep Pos
Materials science: Anode sep Cathode
They always have a fight

## Slide 11: Working principles of electrochemical cells: materials
anode
cathode
pouch
prismatic
Notes: Terminalology:
Electrical engineering: Neg sep Pos
Materials science: Anode sep Cathode
They always have a fight

## Slide 12: Working principles of electrochemical cells:

## Slide 13: Outline
Overview of physics-based modelling
Working principles of electrochemical cells
Survey of commercial/open-source tools
Challenges of physics-based models
Single particle model (SPM)
  Solid-state diffusion
  Ion exchange kinetics
Reduced order modelling
  Numerical methods
  Single bucket model

## Slide 14: Physics-based modelling packages: survey
20+ packages
  Propiriatary
  Open-source
Economics
  languages
  Developing team
  Eco-system

## Slide 15: Challenge 1: parameterisation
Accurate parameterization ensures that the model predictions align with experimental data
E.g., an incorrect diffusion coefficient would lead to errors in predicting lithium concentration profiles
However, it is difficult to capture real-world variability
    temperature-dependent parameters
    ageing-related parameters
    parameter variation due to assumptions
“With four parameters I can fit an elephant.”
- John von Neumann

## Slide 16: Challenge 2: computational complexity
In terms of model order

## Slide 17
Challenge 2: computational complexity
Input
Output
Grey-Box Model
(e.g., nth order RC model)
Black-Box Model
(e.g., ANN model)
White-Box Model
(e.g., P2D model)
In terms of number of parameters
number of parameters
Notes: In general, there are three types of battery models.
Battery dynamics take place in different length-scales and timescales.
These dynamics are fully coupled, and it can be challenging to isolate the individual physics.
These models have very different mathematical structures, corresponding to different fidelity of modelling and application scenarios. However, none of them can individually solve all the BMS problems.

## Slide 18: Outline
Overview of physics-based modelling
Working principles of electrochemical cells
Survey of commercial/open-source tools
Challenges of physics-based models
Single particle model (SPM)
  Solid-state diffusion
  Ion exchange kinetics
  Ageing
Reduced order modelling
  Numerical methods
  Single bucket model

## Slide 19: Single particle model
Two key physics
  Solid phase diffusion
  Ion exchange at the electrolyte-particle interface
Key differences v.s. ECM
  Describe by PDEs with BCs and algebraic equations
  Fixed parameters with no SOC dependence
  Consider the two electrodes separately
  OCP as opposed to OCV

## Slide 20: Single particle model
Key assumptions (in addition to P2D assumptions)
  Single spherical particle representation approximating the porous structure of the electrode material.
  Transport of lithium ion in the electrolyte is fast compared to solid-phase transport, thus neglecting electrolyte diffusion and migration.
  Uniform reaction rate, simplifying the interaction between the particle and the electrolyte (decoupled).

## Slide 21: Single particle model: solid phase diffusion

## Slide 22: Single particle model: solid phase diffusion
3D

## Slide 23: Single particle model: solid phase diffusion
r = 0
r = R
r
1D

## Slide 24: Single particle model: solid phase diffusion
r = 0
r = R
r
1D

## Slide 25: Single particle model: Butler-Volmer kinetics

## Slide 26: Single particle model: Symmetric Butler-Volmer kinetics

## Slide 27: Single particle model: Exchange current density

## Slide 28: Single particle model: Voltage calculation
It is calculated from surface concentration,
not SOC.
Sounds familiar?

## Slide 29: Single particle model: Voltage calculation
What is the equivalent of overpotential in the ECM model from lecture 6?

## Slide 30: Single particle model: simulation
Charge
Discharge

## Slide 31: Single particle model: Ageing
Loss of lithium inventory (LLI)

## Slide 32: Single particle model: Ageing
Loss of active material (LAM)
strain
pressure

## Slide 33: Single particle model: Ageing
Four important ageing-related parameters:

## Slide 34: Lecture 7 Recap
SPM v.s. ECM
  Individual electrode
  Li-ion concentration
  Surface concentration
  Ageing
  Buler-volmer kinetics
  SOC-independent parameters

## Slide 35: Lecture 7 Recap
Four stoichiometry parameters
Physical meaning
Why does c_s(r=R) often go beyond the limits?
2C charge

## Slide 36: Lecture 7 Recap
Four stoichiometry parameters
Physical meaning
Why does c_s(r=R) often go beyond the limits?
4C charge
Concentration gradient
Overpotential
Relaxation

## Slide 37: Lecture 7 Recap
Four stoichiometry parameters
Physical meaning
Why does c_s(r=R) often go beyond the limits?
4C charge
Concentration gradient
Overpotential
Relaxation

## Slide 38: Outline
Overview of physics-based modelling
Working principles of electrochemical cells
Survey of commercial/open-source tools
Challenges of physics-based models
Single particle model (SPM)
  Solid-state diffusion
  Ion exchange kinetics
  Ageing
Reduced order modelling
  Numerical methods
  Single bucket model

## Slide 39: Numerical methods
Example: hat basis function and adaptive meshing

## Slide 40: Numerical methods
E.g. Fourier basis functions
E.g. Lagrangian basis functions
Spectral method
Finite element method (FEM)
Finite volume method (FVM)
…

## Slide 41: Numerical methods: Finite difference method
Some people regard these methods as reduced order modelling (ROM). Why?
r
c
c(r,t)

## Slide 42: Reduced order modelling (ROM)
two-state single bucket model
Li+
anode
cathode

## Slide 43: Reduced order modellin: single bucket model

## Slide 44: Reduced order modellin: single bucket model
Time Evolution of the Average Concentration

## Slide 45: Reduced order modellin: single bucket model
Evaluating the Integral and Using Boundary Conditions

## Slide 46: Outline
Temperature effects
Thermal modelling
Thermal modelling: numerical methods
Lumped thermal model
Thermal management

## Slide 47: Temperature Effects
What determines the capacity?
Q = Q(I, T)
Temperature–dependent parameters
Physical meaning
The greater the temperature of the system, the greater the kinetic energy of the atoms

## Slide 48: Temperature Effects
What determines the capacity?
Q = Q(I, T)
Temperature–dependent parameters
Physical meaning
The greater the temperature of the system, the greater the kinetic energy of the atoms
Arrhenius equation
The frequency of successful jumps

## Slide 49: Temperature Effects
What determines the capacity?
Q = Q(I, T)
Temperature–dependent parameters
Physical meaning
The greater the temperature of the system, the greater the kinetic energy of the atoms
Arrhenius equation
The frequency of successful jumps
where is an activation energy and R is the gas constant. Whereas and are the reference diffusion coefficient and ambient temperature.

## Slide 50: Outline
Temperature effects
Thermal modelling
Thermal modelling: numerical methods
Lumped thermal model
Thermal management

## Slide 51: Why Include Temperature?
Safety and Performance: Excessive heating can degrade battery materials, while low temperatures can significantly reduce power capability.
Thermal Runaway Concerns: In extreme cases, localized heating can lead to thermal runaway if not managed.

## Slide 52: Thermal modelling
Spatially varying temperature
E.g. core temperature
Thermal gradient
Spatially varying parameters
Temperature-dependence
Pouch cells with varying tab locations.

## Slide 53: Thermal modelling
Spatially varying temperature
E.g. core temperature
Thermal gradient
Spatially varying parameters
Temperature-dependence
Pouch cells with varying
tab locations.
Y. Zheng, et al. (2023). Thermal state monitoring of lithium-ion batteries: Progress, challenges, and opportunities. Progress in Energy and Combustion Science

## Slide 54: Thermal modelling
Spatially varying temperature
E.g. core temperature
Thermal gradient
Spatially varying parameters
Temperature-dependence
In-plane and through-plane
E.g.

## Slide 55: Thermal modelling: numerical methods
G. Peprah, Y. Huang, T. Wik, F. Altaf & C. Zou. (In revision). Thermal Modelling of Battery Cells for Optimal Tab and Surface Cooling Control. IEEE TCST.

## Slide 56: Thermal modelling: numerical methods
G. Peprah, Y. Huang, T. Wik, F. Altaf & C. Zou. (In revision). Thermal Modelling of Battery Cells for Optimal Tab and Surface Cooling Control. IEEE TCST.
Original PDE
Spectral-Galerkin
Particular Solution Decomposition
ODEs
Time
Integration

## Slide 57: Thermal modelling: mesh-free methods
Teodorescu, et al. (2022). Smart battery technology for lifetime improvement. Batteries.
Physics-informed neural networks (PINNs)
Grid-free and solver-free
Physical constraints determined by PDE

## Slide 58: Outline
Temperature effects
Thermal modelling
Thermal modelling: numerical methods
Lumped thermal model
Thermal management

## Slide 59: Thermal modelling: lumped thermal model
Assuming temperature gradient is small
we can write a simple energy balance in the form:
where,

## Slide 60: Thermal modelling: lumped thermal model
Assuming temperature gradient is small
we can write a simple energy balance in the form:
The total heat generation rate per unit volume, can be decomposed into several contributions:

## Slide 61: Thermal modelling: lumped thermal model
Reversible (Entropic) Heat
Where,
the terms in the bracket measure how temperature shifts the equilibrium voltage of each half‐reaction, which in turn dictates how much entropic heat is absorbed or released when the cell is operated at different temperatures.
L is the total thickness of the electrode sandwitch

## Slide 62: Thermal modelling: lumped thermal model

## Slide 63: Thermal modelling: lumped thermal model
Convective Cooling Term
Newton (convective) cooling boundary condition

## Slide 64: Outline
Temperature effects
Thermal modelling
Thermal modelling: numerical methods
Lumped thermal model
Thermal management

## Slide 65: Thermal management
Temperature
Dynamic performance
Energy efficiency
Health and lifetime
Thermal safety
charging

## Slide 66: Thermal management
Advantages
Low cost
Simplicity
Disadvantages
Poor thermal performance
Moving parts (noise)
Air cooling
Good thermal performance
High efficiency
Potential leakage
Increased weight
Uniform temperature distribution
No moving parts
Potential leakage
Increased weight
Compact
High efficiency
Costly
Small contact area
Liquid cooling
Phase change materials
Heat pipes

## Slide 67: Thermal management
Cooling plate designs
Simulations

## Slide 68: Thermal management
Cooling plate arrangements

## Slide 69: Thermal management
Commercial cooling channel designs
Hyundai Group's Electric-Global Modular Platform (E-GMP)